## Slide 1: Industrial robot in harsh conditions
Kin Tung
Eren Pekgöz
Daniel Pedraglio O'Hara

## Slide 2: Current Project Status

## Slide 3: Project Schedule Update

## Slide 4: Quick recap on requirements
Main Goal:
  Design a robot to assemble rock bolts (Rebar + Steel Plate)
Environmental Conditions
  Operating Environment: Indoor and outdoor.
  Temperature Range: –40 to +40 °C.
  Lighting Conditions: All lighting conditions, including direct sunlight and complete darkness.
  Environmental factors: Dust, mud, moisture, snow and rain.
Specification of materials
  Steel Plate:
    Dimension: 200x200x8 mm
    Weight: 2.51kg
  Rebar:
    Dimension: 25mm Dia x 3000mm long
    Weight: 11.56kg
Steel Weight Calculator, Steel Express
https://www.steelexpress.co.uk/steel-weight-calculator.html

## Slide 5: System Architecture

## Slide 6: Process Flow
Step 1: Initialisation of system.
Step 2: Robot picks up plate.
Step 3: Robot places the plate on the bolt tray.
Step 4: Repeat step 2 and 3 until 4 plates are placed on the bolt tray.
Step 5: Robot places the rebar on the bolt tray.
Step 6: Robot pushes the rebar into the plate.
Step 7: Repeat step 5 – 6 until bolt tray has 4 assembled rebars.
Step 8: Robot returns to home position and stand by.

## Slide 7: Bolt Tray
Material: Steel construction for durability and strength
Temperature Resistant: Can operate in both high and low temperature environments
No moving parts: Ensures reliability, reduces maintenance need
Fail-safe: Rebars remain secure even in power outages

## Slide 8: Sensors on Bolt Tray
Sensor Type | Advantages | Disadvantages
Inductive Proximity Sensor | No moving parts, detects metal | Cannot detect non-metallic foreign objects
Limit Switch | Easy implementation, no calibration | Mechanical wear
Weight Sensor | High accuracy | Require a rather complex mechanical design of the bolt tray compared to other sensors
Laser Distance Sensor | 2 sensors are enough for the entire tray | Does not perform well with cylindrical or round objects

## Slide 9: Proposed Sensor
Pepperl+Fuchs NBN40-L2-E2-V1:
Operating Distance 0...44mm
Normally Open Switch Mechanism
10-30V DC Operating Voltage

## Slide 10: End Effector (1/3)
Functions:
  Pick and plate rebar
  Pick and plate metal plate
  Push rebar into the plate

## Slide 11: End Effector (2/3)
Magnetic Gripper
  Magnetic force stronger in low temperature
  No external moving parts
    Lubrication not necessary => No frozen lubricant problem
    No frozen joint problem in wet, sub-zero temperature
Pneumatic Magnetic Gripper
  Permanent magnet
  Fail-safe design
    pneumatic pressure/power = off
    no pneumatic pressure/no power = on
IXTUR MRP-20NK
IP67
Lifting capacity with Safety Factor 3 = 13kg for solid round object (ø≥14mm)
https://www.smcworld.com/newproducts/en/mhm/images/02b.jpg
IXTUR MRP-20NK Brochure
https://www.ixtur.com/wp-content/uploads/2023/08/Brochure_MRP-20NK_ENG112018.pdf

## Slide 12: End Effector (3/3)
Rest of the end effector made of 304 stainless steel or other non-magnetic materials
Ver. 0
Ver. 0.1
Ver. 0.2

## Slide 13: Robot Manipulator Requirements
Reach from edge of structure with end effector: 1920 mm.
Good work envelope for objects near and up to 400 mm below it.
Payload of 15,5 kg at 1155 mm.
Available in Visual Components.

## Slide 14: Robot Manipulator (1/2)
ABB IRB 4600-45/2.05
Reach: 2.05m
Payload: 45kg
IP67

## Slide 15: Robot Manipulator (2/2)
Electrical connection: 200-600 V, 50-60 Hz
Weight: 445kg
Operating temperature: 5° to 45° C
  Will require heating in colder environments
Humidity: max 95%

## Slide 16: Alternative Robot Manipulators
Kuka KR 50 R2100
  5 kg more payload, 51mm more reach, operates from 0° to 55° C.
  Almost 20% heavier.
Fanuc M-710/50-20C-5X
  5kg more payload, operates from 0° to 45° C.
  20% heavier, less humidity allowed, worse work envelope due to 5 joints

## Slide 17: Simulation

## Slide 18: From Now to Next Progress Review
Design v1, build and functional test for end effector and bolt tray*
Coding robot manipulator*
*If we manage to get in touch with our supervisor or Sandvik's representative to discuss prototyping

## Slide 19: Q&A

## Slide 20: Thank you!